## Slide 1
BIOFUEL HEALTH INDEX & COMMINGLING FRAMEWORK
Engineering proof of concept • P Saashkintan • SIT / PSA Marine context
01 PROBLEM & AIM
Biofuel quality can change during storage and handling. Repeated topping-up complicates tracking of residual fuel history.
Aim: develop a transparent Python tool that combines fuel-quality indicators with recursive effective-age bookkeeping.
02 ENGINEERING METHOD
• Literature-informed hazard identification
• FMEA: six illustrative failure modes
• MCDA: editable parameter ratings and weights
• BHI: water + TAN + oxidation stability
• Separate reference-limit breach check
• Recursive volume-weighted fuel age
03 TESTING & LIMITATIONS
16 / 16 Python tests passed
Illustrative age example: 6.0 days after replacing 800 L of 1,000 L.
No operational fuel samples. FMEA and MCDA ratings and BHI penalties are provisional. No fuel safety certification is implied.
NEXT: supervisor review → verified fuel-grade limits → laboratory comparison
Sources: McCormick & Moriarty (NREL, 2023); ISO 8217:2024; MPA Singapore biofuel bunkering guidance; IEC 60812:2018